## Slide 1
Programming Design
ROBOTC Software
© 2012 Project Lead The Way, Inc.
Principles of Engineering

## Slide 2: Behavior-Based Programming
A behavior is anything your robot does
  Example: Turn on a single motor or servo
Three main types of behavior
  Complex behavior: Robot performs a complex task
  Example: automate fan control
  Simple behavior: Robot performs a simple task
  Example: fan stops when sensor is activated
  Basic behavior: Single command to a robot
  Example: start a motor
Complex behaviors are broken down into simple behaviors, which are broken down into basic behaviors

## Slide 3: Complex Behaviors
Describe a task or overall goal that a program will accomplish
  A fan runs until someone needs it to stop.
  A safety device warning light turns on before a fan turns on.
  Another light indicates that a fan has stopped.
This can be described as one or more complex behaviors

## Slide 4: Creating Pseudocode
Break down behaviors into individual actions
Do not be concerned about syntax or which commands will be used with ROBOTC
Simply describe them in short phrases
Example
  Turn a motor on for three seconds
  Follow a line until it runs into a wall

## Slide 5: Simple Behaviors
Break each complex behavior down into simple behaviors
List simple behaviors line by line in the correct sequence
Describe actions and the prompt for each action to start

## Slide 6: Creating Pseudocode
Example
  Warning light turns on before the fan starts for three seconds
  Fan turns on and runs until a button is pressed
  A different light turns on for three seconds before the program stops

## Slide 7: Basic Behaviors
Break each simple behavior down further into basic behaviors
Write in terms of the input and output relative to the device

## Slide 8: Creating Pseudocode
Example
  Program starts
  Light 1 (LED 1) turns on for three seconds
  Fan (Motor 1) turns on until a button (bumper switch) is pressed
  Light 2 (LED 2) turns on for 3 seconds
  Program ends

## Slide 9: Identify Inputs and Outputs
Identify the ports by which each input and output will be connected to the Cortex
Be conscious which sensors are analog and which are digital
Label a planning diagram

## Slide 10: PLTW ROBOTC Program Template
Open Sample Program PLTWtemplate
Enter an initial task description of the overall program goal in terms of complex behaviors
Enter pseudocode in terms of basic behaviors in the pseudocode section of the PLTW ROBOTC program template
Notes: Select File, Open Sample Program. Navigate to the PLTW folder. Select the PLTWtemplate file, then select Open.

## Slide 11: PLTW ROBOTC Program Template

## Slide 12: Program Design
Enter label for inputs and outputs in the Motors and Sensors Setup window and change drop down to identify
Use the Program Debugger to confirm that all inputs and outputs are working as expected

## Slide 13: Motor 2 for 5 Seconds
Notes: This example is best demonstrated using the test bed.

## Slide 14: Motor 2 for 5 Seconds

## Slide 15: Motor 2 for 5 Seconds

## Slide 16: Motor 2 for 5 Seconds

## Slide 17: Motor 2 for 5 Seconds

## Slide 18: Program Design
Generally basic behaviors combine to create a complex behavior
Troubleshoot basic behaviors individually as method of troubleshooting a complex behavior

## Slide 19: Program Design
Create code and test small behaviors or sets of behaviors individually
Edit or add comments as you build code

## Slide 20: Program Design
Continue programming while testing individual behaviors
Temporarily turn sections of code into comments using /* followed by */

## Slide 21: Program Design
Sections of code can also be temporarily turned into comments using Toggle Comment using a right mouse click

## Slide 22: Sample Programs

## Slide 23: ROBOTC Natural Language
Language developed especially for PLTW
Lines of code for common robot behaviors are consolidated into single commands
  forward();
  lineTrackforTime();
  stop();
  untilBump();

## Slide 24: ROBOTC Natural Language
Natural Language PLTW is a ROBOTC Platform Type

## Slide 25: ROBOT Motion
Commands that cause the entire robot to perform a behavior

## Slide 26: Movement
Commands that allow control of individual motors or servos

## Slide 27: Motor Reversal
Reversing motor polarity
  Check Reverse in Motors and Setup
  Change speed + / - in program
startMotor(rightMotor, 63);
startMotor(rightMotor, -63);

## Slide 28: Special
Commands that control unique VEX® Hardware: LEDs and Flashlights

## Slide 29: Until
Commands that allow behaviors to be created for the robot to perform until an event occurs such as:
  Button Press
  Encoder Count Reached

## Slide 30: Wait
Commands that wait for an amount of time measured in seconds or milliseconds

## Slide 31: Wait States Accuracy
Motor Speed is affected by battery power
  Motors rotate faster when using a fully charged battery
  Motors rotate slower when using a partially depleted battery
  Device or robot does not move consistently as the battery power drains

## Slide 32: Touch Sensors
Digital sensor
  Pressed = 1 and Released = 0
Caution
  When sensor is pressed or released, its value may rapidly bounce between 0 and 1 briefly
  A brief wait command can reduce the bounce effect

## Slide 33: References
Carnegie Mellon Robotics Academy. (2017). ROBOTC. Retrieved from http://www.robotc.net