## Slide 1
Introduction to the
VEX® Robotics Platform and ROBOTC Software
© 2012 Project Lead The Way, Inc.
Principles of Engineering

## Slide 2: VEX® Robotics Platform: Testbed for Learning Programming

## Slide 3: VEX® Structure Subsystem
VEX® Structure Subsystem forms a robot base
Contains square holes on a standardized ½ in. grid
Allows VEX® components to be assembled in various configurations
Notes: This is a very brief overview of the VEX robotics platform. Refer to the Inventor’s Guide shown in the student resources for more details.

## Slide 4: VEX® Structure Subsystem
Metal components directly attached using 8-32 screws and nuts
  Nylock nut has a plastic insert to prevent unscrewing
  KEPS nut has a ring of “teeth” on one side to grip the piece being installed
  Regular nut has no locking feature
Nylock
Nut
KEPS
Nut
Regular
Nut
8-32 screws

## Slide 5: VEX® Motion Subsystem
Components which make a robot move
  Gear
  Wheel
  Motor
  Servo
Motor
Servo
Gears
Wheels

## Slide 6: VEX® Motion Subsystem – Motors
2-wire motor 269 and 2-wire motor 393
Two methods to connect to Cortex
  Motor ports 1 and 10
  Motor port 2-9 using Motor Controller 29
  2-Wire 269
  2-Wire 393
  Controller 29
Notes: Two-wire motors connect directly to Cortex motor ports 1 and 10. A Motor Controller 29 is needed to connect to Cortex motor to port 2 – 9.

## Slide 7: VEX® Motion Subsystem – Servos
Similar appearance to a motor
Operation is significantly different
  Motor spins continuously at a power value
  Servo rotates to a position between 0o to 120o degrees

## Slide 8: VEX® Sensors Subsystem
Analog Sensors:
  Light Sensor
  Potentiometer
  Line Follower
Digital Sensors:
  Bumper Switch
  Limit Switch
  Optical Shaft
  Encoder
  Ultrasonic Range
  Finder
Provide inputs to sense the environment

## Slide 9: Potentiometers
How It Works
  Analog sensor
  Measures rotation of a shaft between 0 and ~265 degrees
  Cortex returns values between 0 and ~4095
Caution
  Internal mechanical stops prevent potentiometer from turning a full revolution
  Excess torque against the internal mechanical stops will cause them to wear away
Notes: Excess torque against the internal mechanical stops by hand or by a VEX motor will cause the stops to wear away. The potentiometer will continue to function but will have a range between the positions where mechanical stops were located. This is known as a dead zone. In this range, values are not sensed.

## Slide 10: Optical Shaft Encoders
How It Works
  Digital counting sensor
  Inner shaft spins as the encoder measures angle of revolution
Capabilities and Resolution
  360 counts per revolution
  Counts up and down
  The distance which a robot moves can be controlled by monitoring the angle at which the wheels attached to the shaft encoder spin

## Slide 11: Ultrasonic
How It Works
  Similar to how bats and submarines
  sense distance
  Digital sensor returns distance values between 0 and 255 inches or the equivalent centimeters or millimeters
  Returns values of -1 or -2 if used outside of this range or if a return signal is not sensed

## Slide 12: Ultrasonic Range Finder
Ultrasonic Range Finder detects objects in a “cone” field of view
Sensor detects object distance from the center of the sensor
Sensor distance calculations based on sound waves
  Objects that may not be detectable include soft objects that absorb sound, sharp objects that deflect sound, etc.
Notes: Do not use the ultrasonic sensor as the very first command of a program. Until the first sound echo returns to the sensor, it will have a value of -1. A simple delay at the beginning of your program solves this.

## Slide 13: VEX® Cortex Microcontroller
VEX® Cortex (VEX® 2.0)
12 Digital Ports
  Bumper Switch
  Limit Switch
  Optical Shaft Encoder
  Ultrasonic Range
  Finder
  Digital Ports

## Slide 14: VEX® Cortex Microcontroller
VEX® Cortex (VEX® 2.0)
12 Digital Ports
8 Analog Inputs
  Potentiometer
  Line Follower
  Light Sensor
  Analog Ports

## Slide 15: VEX® Cortex Microcontroller
  2 Wire 269
  2 Wire 393
  Controller 29
  VEXnet
  Wireless Key
  Motor Ports
VEX® Cortex (VEX 2.0)
12 Digital Ports
8 Analog Inputs
VEXnet Connection
10 Motor Ports
  Ports 1 and 10 are 2-wire DC ports
  Ports 2 through 9 are 3-wire pulse width modulated (PWM) ports
Notes: VEXnet connection via USB cable or wireless key for remote control and wireless programming. VEX® hardware extends beyond the PLTW classroom kit to support hardware such as an external LCD screen and video camera.

## Slide 16
Return to Activity

## Slide 17: ROBOTC Software
ROBOTC developed specifically for classrooms and competitions
Complete programming solution for VEX® Cortex and several other popular robot platforms
Real-time debugger
Similar to industry-standard C Programming

## Slide 18: Industry Standard Coding
ROBOTC programming is a key component of industry-standard programming languages

## Slide 19: Industry-Standard Skillsets
Java and C++, along with the Eclipse and Visual Studio IDEs, have been used to program:
  Microsoft® Windows OS
  Mac OSX
  US Navy UAV Drones
  Flight Simulators
  DVD Player Firmware
  Video Games
  Microwaves
  CAT Scanners
  Smart Cars
  Satellites
  Cell Phones
  Electronic Toys
  ROBOTC

## Slide 20: ROBOTC Start Page
Open ROBOTC for VEX Robotics
Display of the latest ROBOTC news, version of ROBOTC, and ROBOTC Resources

## Slide 21: VEX Cortex and Natural Language
Change the Platform Type to VEX 2.0 Cortex
Change the Platform Type to Natural Language PLTW

## Slide 22: Sample Programs
Over 75 ROBOTC Sample programs, organized by robot behavior

## Slide 23: Comments
Comments are used to make notes in code for the human programmers
Every sample program contains comments pertaining to robot configuration, ROBOTC commands, robot behavior, etc.
// Single line comment – All material after “//” is ignored by the ROBOTC compiler
/* Multi-line comment*/ – All material between the “/*” and “*/” symbol is ignored by the ROBOTC compiler

## Slide 24: ROBOTC Help
In-depth explanations about ROBOTC installation, commands, debugger, etc.

## Slide 25: Text Function Library
Available functions are listed with a description
List of available functions will expand or shrink depending on the menu level

## Slide 26: Menu Level
Customizes the ROBOTC interface and Text Function Library based on user’s experience level
Select File and then New or select the New File icon to begin creating a program

## Slide 27: Motors and Sensor Setup
Open Motor and Sensors Setup and update to match the physical configuration
OR

## Slide 28: VEX® Cortex Download Method
Allows you to specify:
  How programs are downloaded
  Whether the Cortex looks for VEXnet connection when it starts up
  The VEXnet or USB option will result in the Cortex looking for a VEXnet connection for up to10 seconds before running code

## Slide 29: ROBOTC Color Coding
ROBOTC is color coded to distinguish elements of the program as shown

## Slide 30: References
Carnegie Mellon Robotics Academy. (2017). ROBOTC. Retrieved from http://www.robotc.net
VEX Robotics. (2017). ROBOTC. Retrieved from http://www.vexrobotics.com